## Slide 1
SCIENTIFIC COMPUTING FOR BUILDING ENGINEERING​
Final Presentation G14​
01 September 2025​
POLITECNICO DI MILANO – SCIENTIFIC COMPUTING FOR BUILDING ENGINEERING
G14: FARNAZ VAFA – JACOPO GUERRINI – MOHAMMAD SHOJAEE – SALMA YANUAR​
241022_SCBE_FinalPresentation_G14​
PAGE 1

## Slide 2
Team 14
PAGE 2
Farnaz Ahmadi Vafa (FV)​
Civil Engineer​
Mohammed Amin Shojaee (MS)​
Civil Engineer​
Salma Nabilah Yanuar (SY)​
Architect​

## Slide 3
This project focuses on optimizing the solar performance of twisted high-rise towers. Using the Turning Torso in Malmö as a case study, we applied parametric design, environmental simulation, and emulator modeling tooptimize the rotation and L1 in order to get close as possible to the design Value of 6000 kWh
PAGE 3
Turning Torso

## Slide 4
Twisted towers interact with sunlight differently from straight towers. In real projects, perimeter constraints often limit design freedom. Previous research hasn’t fully explored how floor rotation and geometric proportions interact to affect solar gain. Turning Torso gives us a real-world, iconic example for testing.
  Twisted towers = unique solar patterns.
  Fixed perimeter floor plans are common in real design.
  Gap: No combined analysis of rotation + proportions.
  Turning Torso is an ideal test case.
PAGE 4
Background and Problem

## Slide 5
Objectives
TEST IMPACT OF FLOOR ROTATION AND PROPORTIONS
OPTIMIZE FOR 6000 KWH ON 21 DEC (WORST DAY)
COMBINE SIMULATION + EMULATOR FOR EFFICIENCY
CREATE A FLEXIBLE WORKFLOW FOR OTHER TOWERS
PAGE 5
Our goals were to understand how geometry affects solar performance, optimize the design for a specific energy target, and build a workflow that can be reused for other twisted towers.

## Slide 6
SIMULATION WITH LADYBUG TOOLS (MALMÖ EPW)
2
PARAMETRIC MODELLING IN GRASSHOPPER
1
PAGE 6
Methodology Overview
EMULATOR IN PYTHON
3
OPTIMIZATION WITH POWELL METHOD AND MINIMIZE FUNCTION
4
AUTOMATED GEOMETRY CONTROL AND DATA COLLECTION
5
We built a fully parametric model in Grasshopper, used Ladybug Tools with Malmö climate data for simulations, created a polynomial emulator in Python to speed up predictions, and ran an optimization algorithm to find the best design.

## Slide 7
PARAMETRIC MODELLING IN GRASSHOPPER
1
PAGE 7
  A single floor plan was abstracted as a pentagon with alternating sides L1 and L2.
  L1 was manually varied, L2 was auto-calculated to keep perimeter P constant.
  Floor rotation (θ) was applied to simulate twisting across tower height.
  Internal angles (b, c) updated automatically to maintain valid geometry.
L1 values (meters):
16, 17, 18, 19, 20, 21, 22, 23
Rotation angles (°):
10 to 120 (step of 10°)
Total configurations tested: 96 (in original case study)
Model built in Grasshopper for Rhino; phyton code controlled L1 and rotation angle to generate valid and diverse floor geometries for solar simulation.

## Slide 8
FORMALIZATION OF THE ADDRESSED PROBLEM
2
PAGE 8
  Initial Optimization Objective:
  Loss Function (for emulator training):
  Optimization type:
    Simulation-based with emulator approximation
  Total configurations simulated: 96
  The goal is to find the best L1 and rotation (θ) that near to to the target value of solar irradiation on the façade.
  The floor is a five-sided polygon with alternating sides L1 and L2.
  L2 is calculated to keep perimeter constant using:
  Solar irradiation is represented as I(L₁, θ), estimated using emulator.
  The optimization domain is:
    L₁ ∈ [16, 23] meters
    θ ∈ [10°, 120°]
This problem is approached as a black-box optimization task where L1 and θ are inputs. Solar irradiation is predicted using a trained emulator, and the best combination is selected based on the minimum error.

## Slide 9
EMULATOR IN PYTHON
3
Purpose
  Fast prediction for new L1, θ combinations
  Design exploration without re-running simulations
  Speed up optimization routines
  Find the best polynominal that fits well based on the original data
THE MAIN PURPOSE
to find a polynomial surface (which has an equation) that fitsthe best to the original dataset so the values between the original dataset that was not calulated can be predicted and interpolated with the higher precision and ther is no need for iterating and modeling the builidng for all the values
PAGE 9
  Emulator replaces slow simulations with fast prediction.
  Trained on 96 configurations (L1, θ) with Ladybug results.
  Predicts total solar irradiation (including walls, roof, and floor).
  Key inputs:
    L1 = pentagon edge (m)
    θ = floor rotation (°)
The emulator bridges parametric modeling, simulation, and data-driven prediction, supporting real-time performance evaluation.

## Slide 10
PAGE 10
OPTIMIZATION WITH POWELL ALGORITHM
4
  Goal: Find L1 and θ that get close to 6000 kWh on Dec 21
  Polynomial surface from emulator used in optimization
  Error function:
Solver: Powell’s algorithm (SciPy)
  L1 ∈ [16, 23] meters
  θ ∈ [10°, 120°]
Instead of maximizing a global peak, the optimizer finds the closest match to the required energy target, improving design realism
AUTOMATED GEOMETRY CONTROL AND DATA COLLECTION
  Python replaced manual Grasshopper inputs
  L1 and top vertex coordinates calculated using math formulas
  Geometry auto-updates to satisfy fixed perimeter
  α kept fixed; L2 recalculated from L1
  Script 1:
    Controls L1, θ, floors, and location
    Run and control by a trigger
    Iterates over full range with delay
  Script 2:
    Collects total incident irradiation + surface area
    Stores full dataset in CSV (6 values per row)
Python scripting reduced manual work, ensured consistency, and enabled large-scale testing of geometric and environmental combinations.
5

## Slide 11
Results : Parametric Modelling
PAGE 11
Apply Progressive Floor Rotation
  Multiply base angle θ by floor index to simulate twist.
  Use Rotate and DegToRad to apply rotation
2
Generate Tower Geometry
  Use the Series component to define Z-heights for each floor (every 4 meters).
  Apply Move to vertically stack identical pentagonal floor plates.
1
Calculate Surface Area
  Use the Area component to calculate each face.
  Apply Mass Addition to sum values and get the total façade surface area.
Create Tower Shell
  Apply Loft to connect all floors into one continuous surface.
  Use Cap Holes to close the geometry, forming a solid for analysis.
3
4
Simulate Solar Irradiation
  Import EPW climate data (Malmö) via Ladybug.
  Convert geometry to mesh for per-face solar evaluation.
  Visualize cumulative irradiation using Ladybug irradiation analysis, with color mapping
5

## Slide 12
Climate Setup
  Used EPW weather data for Malmö
  Simulated worst-case solar day: 21 December
  Target: 6000 kWh irradiation to meet energy needs year-round
1
Solar Context & Temperature
  Analyzed dry bulb temperature distribution
  Coldest zones: North/Northeast
  Warmest exposure: South-facing
2
Radiation Contour Plot
  Highest irradiation at low rotation (10°–50°) and longer L1
  L1 > 20 m gives consistently higher values
3
Results : Radiation Analysis
PAGE 12
Performance Insight Through Climate-Based Simulation

## Slide 13
Rotation Sensitivity (L1 = 23 m)
  Sharp drop in performance after 50° rotation
  Confirms self-shading and misalignment at high angles
4
Heatmap Visualization
  Visualizes performance gradient
  Red zone (top-left) = best config (low rotation, high L1)
  Steep drop-off beyond 60°
5
3D Surface Plot
  Clear peak at L1 = 23 m, θ = 10°
  Decline along rotation axis = high impact of twisting
6
PAGE 13
Rotation impacts solar gain more than L1 Best config: L1 = 23 m, θ = 10°
Performance-focused geometry requires early parametric evaluation

## Slide 14
Results : Emulator Model Development
PAGE 14
From Simulation to Prediction
1
Polynomial Regression Setup (second degree)
  Starting from the simpleased surface equation with 2 degree
  valuate the error between the original data and the corrisponding point on polynomial surface
  Try to reduce this error by using higher degree surfaces; this, was done by evaluating the R2 and MSE of the model and org. dataset
  At the end by cross validation we found the the equation degree that has the highest R2 and and lowest MSE

## Slide 15
2
Evaluate 2nd-Degree Model
  SSE reduced by 80.2%, but error remained in high-radiation zones
  Error heatmap revealed performance drop in complex zones
Results : Emulator Model Development
PAGE 15
From Simulation to Prediction

## Slide 16
3
Upgrade to 5th-Degree Model
  Added full polynomial terms up to degree 5 (21 features)
  7-fold cross-validation used to avoid overfitting
  Best fit at degree = 5:
    MSE: 506,130 ± 192k
    R² = 0.785
Results : Emulator Model Development
PAGE 16
From Simulation to Prediction

## Slide 17
4
Accuracy Improvement
  SSE dropped by 88.6% → better than 2nd-degree
  Visual results: tighter cluster along y=x
Results : Emulator Model Development
PAGE 17
From Simulation to Prediction

## Slide 18
5
Local Error Heatmap
  Lower error in low rotation zones
  Some localized overfitting in high rotation/high L1 areas
Results : Emulator Model Development
PAGE 18
From Simulation to Prediction

## Slide 19
5
Test Predictions & Global Optimum
  Known input (20°, 20m):
    5th-degree: 6900.63 kWh
    Actual: 6909.38 kWh
  Best config:
Results : Emulator Model Development
PAGE 19
From Simulation to Prediction
  5th-degree emulator captures non-linear behavior
  Enables fast and accurate prediction without simulation
  Supports design space exploration and optimization
Conclusion

## Slide 20
1
Define the Objective Function
  Goal: minimize squared error from target radiation (6000 kWh)
  Error function:
  f̂ is the 5th-degree emulator predicting radiation
2
3
Optimization Results
  Converged at:
    Rotation: 53.15°
    L₁ length: 22.13 m
    Radiation: 6000.00 kWh
    Error²: 0.0000
Results : Optimization
PAGE 20
Finding the Geometry That Achieves 6000 kWh
Set Up SciPy Optimizer
  Optimizer: scipy.optimize.minimize using Powell method
  Bounds:
    r ∈ [10°, 120°]
    L₁ ∈ [16 m, 23 m]
  Start point: previously found maximum (10°, 23 m)
Final Irradiation Value
5999.89 kWh

## Slide 21
4
5
Visualize Error Zones
  Blue regions = (r, L1) pairs close to 6000 kWh
  Red regions = high error
  Shows optimizer’s local convergence despite multiple near-optimal basins
PAGE 21
Understand Variable Sensitivity
  Error vs Rotation (at fixed L₁ = 22.13)
  Error vs L₁ (at fixed r = 53.15)
  Shows how optimization “locks in” variables that minimize deviation
Using a 5th-degree emulator + Powell optimization, we precisely reached the 6000 kWh target The optimizer identifies one solution, even though multiple may exist, due to stopping criteria and local minimal, This confirms the workflow is accurate, efficient, and ready for use in performance-driven parametric design

## Slide 22
Results : Optimized Floor Plan Design
PAGE 22
From Initial Geometry to Solar-Optimized Solution
Initial Shape (left) : Regular pentagon with equal side lengths and no rotation
Parametric Variations (middle) : Generated by adjusting L1 and L2 while keeping perimeter constant → Explored entire design space in Grasshopper
Simulation & Emulator : Each configuration evaluated with Ladybug → Trained polynomial emulator
Optimization (right) : Python + Powell method → Found floor plan with 6000 kWh irradiation
Final Geometry : Optimized proportions and rotation yield high-performance floor design

## Slide 23
PAGE 23
Innovation and Broader Implications
  This study presents a novel method to analyze twisted towers.
  Parametric model + online platform = no advanced modelling expertise required.
  Enables direct input of parameters to estimate solar irradiation and surface area
Automatic Iteration in Python
Malmo
Sweden
Milan
Italy
Barcelona
Spain
Berlin
Germany
Different EPW
Further improvement by using different cities EPW

## Slide 24
PAGE 24
Innovation and Broader Implications
Base Geometry based on Phyton Code
Context-Based Radiation Analysis
The local shade of nearby building might affect the total irradiation fall on the building facade, hence we assign the context for higher precision irradiation analysis

## Slide 25
PAGE 25
Innovation and Broader Implications
User-friendly Interface
To extend the flexibility of the parametric workflow, a user-friendly interface was developed using Python. This platform allows users to select the city (e.g., Barcelona, Malmö, Milan), floor shape (pentagon, square, hexagon), and geometric inputs like L1 and rotation angle. The application instantly calculates the expected irradiation, making the optimization process accessible without needing to open Rhino-Grasshopper or run simulations manually.

## Slide 26
Conclusion
PAGE 26
This project explored how parametric modeling and emulator-based optimization can guide solar-responsive design in twisted high-rise towers. Using the Turning Torso in Malmö as a case study, we found that low rotation angles (around 10°) and longer floor edges (L1 = 23 m) maximize solar gain. By training a fifth-degree polynomial emulator, we achieved high predictive accuracy (88.6% SSE reduction), enabling fast and precise optimization toward a 6000 kWh radiation target.
While some local prediction errors remain, the workflow—combining Grasshopper, Ladybug, Python, and SciPy—proves flexible, efficient, and scalable. It contributes not only to sustainable tower design in low-sun climates, but also to broader applications of data-driven geometry in architecture

## Slide 27
Turning Torso